## Slide 1: “In the beginning was the word, and the word was two bytes”
LING 516
Week 2

## Slide 2
COMPUTER
INFORMATION
processes
log2(x)
defined
BITS
measured
DIGITAL
is
using
LOGIC
TRUTH VALUES
works with
equivalent
PROGRAMMABLE
is
PROGRAMMER
represents
by
ELECTRONIC
is
BINARY DIGITS
equivalent
numbers are represented using
How to represent time? colors? texts? sounds?

## Slide 3: Plan for Today:
Representing (whole) numbers
  Adding and subtracting numbers
Representing time
Representing colors: RGB
Representing texts: ASCII and Unicode
Representing sounds: WAV

## Slide 4: Representing (whole) numbers
Whole numbers are easy to represent using the binary system
How to trick the computer into doing arithmetic operations with numbers?
  Addition
  Multiplication
  Subtraction
  Division
When we talk about one-bit numbers:
  addition is the same as exclusive disjunction (XOR)
  multiplication is the same as conjunction (AND)

## Slide 5: Addition vs. XOR
0 XOR 0 = 0 0 + 0 = 0
0 XOR 1 = 1 0 + 1 = 1
1 XOR 0 = 1 1 + 0 = 1
1 XOR 1 = 0 1 + 1 = 0 (and 1 is carried over)

## Slide 6: Multiplication vs. AND
0 AND 0 = 0 0 * 0 = 0
0 AND 1 = 0 0 * 1 = 0
1 AND 0 = 0 1 * 0 = 0
1 AND 1 = 1 1 * 1 = 1

## Slide 7: Binary addition: more than 1 bit
Let’s see how the computer adds numbers that are longer than 1 bit.
Problem: 2 + 3 = ?
 | 23=8 | 22=4 | 21=2 | 20=1
210 = | 0 | 0 | 1 | 0
310 = | 0 | 0 | 1 | 1

## Slide 8: Binary addition
 | 23=8 | 22=4 | 21=2 | 20=1
210 = | 0 | 0 | 1 | 0
310 = | 0 | 0 | 1 | 1
Add 00102 + 00112

## Slide 9: Binary addition
 | 23=8 | 22=4 | 21=2 | 20=1
210 = | 0 | 0 | 1 | 0
310 = | 0 | 0 | 1 | 1
510 = | 0 | 1 | 0 | 1
Add 00102 + 00112

## Slide 10: Binary subtraction
We don’t need subtraction if we figure out how to represent negative numbers.
“Two’s complement”:
  Represent the corresponding positive number
  Apply bitwise logical NOT (i.e. invert all bits)
  Add 1 to the result
 | 23=8 | 22=4 | 21=2 | 20=1
310 = | 0 | 0 | 1 | 1
“NOT” | 1 | 1 | 0 | 0
“+1” | 1 | 1 | 0 | 1
= -310

## Slide 11: Binary subtraction
 | 23=8 | 22=4 | 21=2 | 20=1
510 = | 0 | 1 | 0 | 1
-310 = | 1 | 1 | 0 | 1
Calculate 5-3 = 5+(-3)

## Slide 12: Binary subtraction
 | 23=8 | 22=4 | 21=2 | 20=1
510 = | 0 | 1 | 0 | 1
-310 = | 1 | 1 | 0 | 1
 | 0 | 0 | 1 | 0
Calculate 5-3 = 5+(-3)

## Slide 13: How many bits to use?
8 bits = 1 byte
  Can represent integers 0..255 (unsinged) or -128..+127 (signed)
16 bits = 2 bytes = 1 word
  Can represent integers 0..65535 (unsigned) or -32,768..+32,767 (signed)
32 bits = 4 bytes = 1 double word
  Can represent integers 0..4,294,967,295 (unsigned) or -2,147,483,648..+2,147,483,647 (signed)
64 bits = 8 bytes = 1 quad word
  Can represent integers 0..18,446,744,073,709,551,615 or -9,223,372,036,854,775,808..+9,223,372,036,854,775,807

## Slide 14: Representing things other than numbers
Time
Colors
Texts
Sounds

## Slide 15: Time
UNIX Timestamp: Number of seconds that elapsed since the midnight (Greenwich Mean Time) on January 1, 1970
  https://www.unixtimestamp.com/
Do we need signed or unsigned integers to represent time?
Read about the Y2038 problem: https://en.wikipedia.org/wiki/Year_2038_problem
Useful in applications that time responses from the user (assessment, SLA, etc.)

## Slide 16: Colors

## Slide 17: Colors
Intensity of red: 0..255
Intensity of green: 0..255
Intensity of blue: 0..255
Total: 256*256*256 = 16,777,216 colors
RGB representation: three bytes are usually written in hexadecimal, e.g.
  0xFF0000 – pure red
  0xF1BE48 – Iowa State Gold
  0xC8102E – Iowa State Cardinal

## Slide 18: Comprehension check
Represent “white” in RGB

## Slide 19: Texts
American Standard Code for Information Interchange (ASCII)
7 bits (can encode 27=128 different characters)
26 | 25 | 24 | 23 | 22 | 21 | 20
0 | 0 | * | * | * | * | *
Special characters: ASCII codes 0..31 |  |  |  |  |  | 
26 | 25 | 24 | 23 | 22 | 21 | 20
0 | 1 | * | * | * | * | *
Math symbols: ASCII codes 32..63 |  |  |  |  |  | 
26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | * | * | * | * | *
Uppercase: ASCII codes 64..95 |  |  |  |  |  | 
26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 1 | * | * | * | * | *
Lowercase: ASCII codes 96..127 |  |  |  |  |  |